## Slide 1
« DSFLI » definition
A bulb, a led module, emit an amount of light expressed in lumen
The illuminance, expressed in lux, is the amount of lumen reaching a given area, divided by the surface of this area: 1 lux = 1 lumen/m2 = 1 lm/m2
1m2  900 lux
1000m2  0.9 lux
Light source (bulb, led module) output flux: 1000 lumen
Luminaire output flux: 900 lumen
(luminaire efficiency:90%)

## Slide 2
« DSFLI » definition
Area intended to be lit:
defined in the Notice issued by the French ministry:
The area intended to be lit corresponds to the useful area which holds movements, people, goods, the lighting of which contributes to promoting safety. Thus, even if illumination of the "surroundings" of the useful surface is desired, they must not be added to the “area intended to be lit” in the calculation of the DSFLI
1m2  900 lux
1000m2  0.9 lux
Light source output: 1000 lm
Luminaire output: 900lm
An area to be lit of 100m2
0 lux
THE « DSFLI »: THE TOTAL LIGHT EMITED BY THE LIGHT SOURCES (BULB, LED MODULE), IN LUMEN, INTENDED TO LIT AN AREA IN M2; IT IS NOT AN ILLUMINANCE, IT IS AN ALLOCATION OR QUOTA OF LIGHT
An area to be lit of 100m2
These two lighting installations show the same « DSFLI »:
1000 lumen produced to lit 100m2
DSFLI = 1000 lm / 100 m2
= 10 lm/m2

## Slide 3
« DSFLI » definition
There, the light is poorly distributed
Here the light overflows excessively from the area to be lit
In both cases, the “DSFLI” concept prevents light source increase or multiplication of light sources; the “DSFLI” challenges to redistribute the light flux in a more efficient way with the same quantity of light
The “DSFLI” sanctions lighting installations that waste light
1m2  900 lux
1000m2  0.9 lux
Light source output: 1000 lm
Luminaire output: 900lm
An area to be lit of 100m2
0 lux
An area to be lit of 100m2
These two lighting installations show the same « DSFLI »:
1000 lumen produced to lit 100m2
DSFLI = 1000 lm / 100 m2
= 10 lm/m2